## Slide 1: Quality Control Concept under Digital Data Collection
Automated Quality Inspection System in Manufacturing Process

## Slide 2: Outlines
Review of pre-class video assignments
  What is a Vision system?
    https://youtu.be/atoUpGgw2fE
  What Is Image Processing?
    https://youtu.be/QMLbTEQJCaI
Traditional Quality Inspection System
Automated Quality Inspection System

## Slide 3: Traditional Quality Inspection System
[Ref] Technical Note. “PREDICTIVE STATISTICAL PROCESS CONTROL”. An update on data-driven CNC machining at L&S Machine Company.
Random Inspection
Samples
Frequency
Process Data
Data Analysis
SPC
Production Process
Work-in-Process
Finished goods
Sample size
Inspection resources
Paper
Excel file
Distribution
Process Capability
Control chart
Software
Excel
Minitab
Check sheet
Measurement system analysis
Data type
Quantity
Appraisal
Feedbacks for Process Improvement

## Slide 4: Case study : Cookies Factory
https://www.delish.com/holiday-recipes/christmas/a25440155/andes-chip-cookies-recipe/
Traditional Inspection steps
Take samples
  How often?
  How many?
Measure
  Dimension
  Weight
Appraise
  Roundness
  Choco. chips spread evenly
  Taste
Record observations
Analyze data
Send feedback to a process
http://eapo-tokyo.org/courses/fsm_17-ag-23-ge-dln-a-03/
Quality Characteristics
Size
weight
Shape
Appearance
Taste

## Slide 5: What if … There is a technique that can
Inspection steps
Take samples
  How often?
  How many?
Measure
  Dimension
  Weight
Appraise
  Roundness
  Choco. chips spread evenly
  Taste
Record observations
Analyze data
Send feedback to a process
Perform 100% inspection with low cost
Complete inspection steps in seconds
Report process performance in real-time

## Slide 6: What if … This concept is affordable
http://pdf.com/exensio-old

## Slide 7: CIMS and AQIS
Computer integrated manufacturing system (CIMS)
  “ A manufacturing system in which all activities relevant to manufacturing are integrated via electronic data collecting and processing frames, Gunn (1998)”
Automated quality inspection system (AQIS) is designed to
  Classify conforming and nonconforming units automatically
  Collect data of the entire units produced
  Assess process performance in real-time
  Reduce resources used in quality inspection
  Reduce human errors in measurement, appraisal, and forgetfulness

## Slide 8: Data Collection System of Automated QIS
Camera
Monitor
Diverter
Hardware
Transportation system
  Conveyor
  Diverter
Sensor
  Cameras
  IR Scanner
Computer
  CPU and Monitor
Software
Internet connection
Database / Cloud design
Inspection algorithm
  Specification
  Reference
  Statistical foundation

## Slide 9: Automated Quality Inspection
https://youtu.be/KXMPk3FKHgA

## Slide 10: Image processing in Automated QIS
Image processing is a common term in vision technology
Applications in Automated QIS are
  Measurement
    Alignment (position/angle)
    Location
    Shape
    Dimension
  Color
  Alien objects
    Defects on fabric/metal

## Slide 11: Benefits of Automated QIS
Minimize operators’ errors
Reduce data collection cost
Reduce process analysis time (Real-time feedback)
Faster respond to assignable causes
  Stop production line immediately after a predetermined number of defects have been reached
  Reduce cost of nonconforming products
Online quality monitoring and assessment

## Slide 12: Impact of Automated QIS to Traditional QIS
Automated SPC report obtained from Automated QIS could affect these following partners
  Quality Inspector (Operator level)
    No longer needed
      All data are automatically recorded
      Appraisal are, well, let’s say, automatically done
  Quality Engineer
    Spend less time on running MSA
      Human errors during inspection are eliminated
    May not need to fully understand the statistical foundation of SPC due to the automatically generated report from a software
      Analysis errors are eliminated
    Must reskill to fully understand the new set of statistical foundation of Automated SPC, where real-time data is used in stead of samples

## Slide 13: Statistical Issues of Automated SPC
Data analysis of a whole population, not just samples
  Sample size is equal to one
Data are auto-correlated
  The assumption of independently and identically distributed data is not satisfied
Non-normality
  The ‘true’ distribution of data is revealed.
These issues require engineers to reskill on how to use
  The new set of control charts for monitoring real-time data
  The new test rules for interpreting the charts

## Slide 14: Conclusions
Automated QIS provides an abundance of data from production process at a lower cost, with faster feedback
Due to the decreasing trend of automation cost and low birth rate, most industry are converting from traditional QIS toward the automated QIS
Under the context of automated QIS, quality engineers should
  Understand the impact of automated QIS
  Be able to manage changes in the transformation (technology, people, technical skills)
  Be able to understand and can interpret SPC report for automated QIS, which is constructed based on a different set of statistical foundation compared to the traditional SPC
Next lecture … The general SPC techniques for monitoring real-time data

## Slide 15: References
D. Q. Cai , M. Xie & T. N. Goh (2001) SPC in an automated manufacturing environment, International Journal of Computer Integrated Manufacturing, 14:2, 206-211.
T. G. GUNN, (1989) Computer integrated manufacturing (CIM) . In C. Machover ( ed.), The C4 Handbook CAD, CAM, CAE, CIM (Blue Ridge Summit, PA: Tab Books) , pp. 319 – 332.
Xie, M., Goh, T. N., & Kuralmani, V. (2012). Statistical models and control charts for high-quality processes. Springer Science & Business Media.
Linker, R. (2008, September). Extension of statistical process control (SPC) methodology to dynamic systems controlled via output feedback. In 2008 IEEE Conference on Cybernetics and Intelligent Systems (pp. 482-486). IEEE.