## Slide 1
Real-Time Quality Control
Module 3: Automated Quality Report System

## Slide 2: What will you learn from this content?
01
Structure and components of the quality control tools and devices
02
Process management of real-time quality control

## Slide 3: In-process Quality Control
Notes: J.D.T. Tannock, 1992, Automating Quality Systems, Chapman & Hall

## Slide 4: In-process Quality Control
Any effective strategy for product quality must involve the use of an appropriate mix of methods, aimed at eliminating the possibility of unsatisfactory items reaching the customer with minimum additional cost
Notes: J.D.T. Tannock, 1992, Automating Quality Systems, Chapman & Hall

## Slide 5: In-process Quality Control
For manufacturing
  Process improvement – to eliminate the possibility of defective items. Eliminating all important causes of process variability.
  In-process quality control – monitoring process parameters or in-process inspection of product.
  Post-process quality control – to detect and filter out defective items. Sampling inspection combined with SPC methods is sufficient to control the majority of processes.
Notes: J.D.T. Tannock, 1992, Automating Quality Systems, Chapman & Hall

## Slide 6: In-process Quality Control
Notes: https://www.aerospacemanufacturinganddesign.com/article/5-questions-with-dan-skulan/

## Slide 7: Examples of Automatic In-process Quality Control
In-cycle gauging with CNC machining
  Most CNC machines incorporate ‘closed-loop’ positional feedback.
  They are fitted with axis measuring scales – sensors to determine the position of the machine slides.
  Use of the computer-controlled axis moves of the machine tool to position cutting tools and take cuts and move a probe which is fitted in place of a cutting tool.
  Touch trigger probes are used to sense the position and size of the cutting tools
Notes: J.D.T. Tannock, 1992, Automating Quality Systems, Chapman & Hall

## Slide 8: Examples of Automatic In-process Quality Control
Notes: https://www.renishaw.com/en/in-process-control--14159

## Slide 9: Examples of Automatic In-process Quality Control
Plastic injection moulding
  Thermoplastic granules are heated, mixed and sheared in a screw preplasticizer until they melt, when they are injected under pressure into a cooled metal mould
  Deviations from the set values (melt temperatures; injection, metering and cycle times; melt cushion; pressure integral and maximum value) can be logged, trigger an alarm, or shut down the process according to the extent by which the process tolerance has been exceeded
  Software produce SPC control charts based on the process data, with automatically calculated limits which trigger action when a trend is detected
Notes: J.D.T. Tannock, 1992, Automating Quality Systems, Chapman & Hall

## Slide 10: Examples of Automatic In-process Quality Control
Notes: Benigno Muñoz-Barron, Luis Morales-Velazquez, Rene J. Romero-Troncoso, Carlos Rodriguez-Donate, Miguel Trejo-Hernandez, Juan P. Benitez-Rangel and Roque A. Osornio-Rios , FPGA-Based Multiprocessor System for Injection Molding Control, Sensors 2012, 12, 14068-14083;

## Slide 11: Case Study
Case#1 Assembly Process Monitoring
Monitoring the high-speed automatic assembly of electrical connectors
  Moulded plastic bodies with holes into
  A flexible computer-controlled manufacturing cell capable of rapid product changeover
  Pins were inserted at a rate of ten per second from a bandolier
  Plastic bodies were located on carriers which move along a conveyer system
Notes: J.D.T. Tannock, 1992, Automating Quality Systems, Chapman & Hall

## Slide 12: Case Study
Case#1 Assembly Process Monitoring
Quality Problems
  Bent or smashed pins
  Incorrect pin end position
  Incorrect pin protrusion
  Insufficient pin retention force
Defects
  An infrequent and apparently random occurrence when there was no identifiable process or material fault
  An increasing incidence of problems when wear or maladjustment in the insertion mechanism was starting to affect the process
Notes: J.D.T. Tannock, 1992, Automating Quality Systems, Chapman & Hall

## Slide 13: Case Study
Case#1 Assembly Process Monitoring
Quality Problems
  Bent or smashed pins
  Incorrect pin end position
  Incorrect pin protrusion
  Insufficient pin retention force
Defects
  An infrequent and apparently random occurrence when there was no identifiable process or material fault
  An increasing incidence of problems when wear or maladjustment in the insertion mechanism was starting to affect the process
Notes: J.D.T. Tannock, 1992, Automating Quality Systems, Chapman & Hall

## Slide 14: Case Study
Case#1 Assembly Process Monitoring
Solution
  A process monitoring with immediate process control feedback
  The assembly force was chosen as the only accessible process parameter
  A front-end processor allow communications with the assembly machine controller
Notes: J.D.T. Tannock, 1992, Automating Quality Systems, Chapman & Hall

## Slide 15: Case Study
Assembly force front-end processor
Notes: J.D.T. Tannock, 1992, Automating Quality Systems, Chapman & Hall

## Slide 16: Case Study
Case #02: Web based cloud solution for support of quality management 4.0 in the concept of industry 4.0
  Objective: Implementation of ICT systems, especially web-based applications, clouds and open source tools for improvement of the quality management
  Industry 4.0 pilar: Big data and analytics, and Cloud systems
Notes: Miladin Stefanović, Aleksandar Đorđević, Hrvoje Puškarić, Miloš Petronijević, 2019, Web based cloud solution for support of quality management 4.0 in the concept of industry 4.0, Quality Festival 2019

## Slide 17: Case Study
Notes: Miladin Stefanović, Aleksandar Đorđević, Hrvoje Puškarić, Miloš Petronijević, 2019, Web based cloud solution for support of quality management 4.0 in the concept of industry 4.0, Quality Festival 2019

## Slide 18: Case Study
Case #03 Unifying Real-time Visibility Across 26 Factories (Nestle Waters)
  System: InfinityQS
  Nestlé Waters meets consumer needs by keeping its wide variety of products flowing through strong distribution channels. The company has emerged as a substantial player in the bottled water market. That leadership position is strengthened by the company’s continuous improvement efforts—starting with a major initiative to improve quality and operational visibility across its production facilities
Notes: InfinityQS, Keeping Success Flowing

## Slide 19: Case Study
Case #02: Unifying Real-time Visibility Across 26 Factories (Nestle Waters)
Before implementation:
Nestlé Waters had been using a cumbersome paper-based system to collect and analyze data. When issues arose that required immediate attention, the company’s quality engineers had to disrupt operators on the production line to retrieve the necessary data.
Notes: InfinityQS, Keeping Success Flowing

## Slide 20: Case Study
Case #03: Unifying Real-time Visibility Across 26 Factories (Nestle Waters)
Implementation:
The Nestlé Waters IT team leveraged InfinityQS Professional Services. These expert services are provided by teams of skilled, certified quality engineers, industrial statisticians, and Six Sigma Black Belts, all with extensive manufacturing experience. They spread the implementation across 16 Retail sites, as well as eight Home and Office sites, and integrated them with corporate headquarters.
Notes: InfinityQS, Keeping Success Flowing

## Slide 21: Case Study
Case #02: Unifying Real-time Visibility Across 26 Factories (Nestle Waters)
Implementation:
Nestlé Waters now has real-time visibility over production processes—both within individual sites and at the corporate level across dozens of factories. By tracking trends in quality data, they are able to make more accurate and timely decisions about process improvements.
It is ultimately easier for the operator. Even with the minimal computer skills many of the operators had in the beginning, the overwhelming consensus is that they prefer using InfinityQS over a paper system.
Notes: InfinityQS, Keeping Success Flowing

## Slide 22: Case Study
Notes: InfinityQS, Keeping Success Flowing

## Slide 23: Case Study
Case #04: How an Elevator Manufacturer Uses Real-Time SPC Data for Process Improvement
Problem: - The tendency to produce out-of-spec elevator wall panels.
- Job site construction delays (2-7 days)
- Wasted installation crew time
- Cost money
Notes: InfifityQS, Elevating Quality to the Top Floor

## Slide 24: Case Study
Case #03: How an Elevator Manufacturer Uses Real-Time SPC Data for Process Improvement
Solution: Implementing ProFicient system at their primary elevator panel manufacturing site to identify when and where panel processes. Prompting shop-floor operators to take immediate correction action.
“Once we put InfinityQS controls in place, we were able to prevent non-conforming material from leaving the factory.”
Notes: InfifityQS, Elevating Quality to the Top Floor

## Slide 25: Case Study
Notes: InfifityQS, Elevating Quality to the Top Floor